QUADRAPOLE DETECTOR CONFIGURATIONS:

SQUARE, RECTANGULAR AND DIAMOND CONFIGURATIONS:

DETAILED INFORMATION ON DETECTOR LOOPS CAN BE FOUND ON STANDARD PLAN 902.50

| CONFIGURATION | TYPICAL USES | ADVANTAGES | DISADVANTAGES |
| --- | --- | --- | --- |
| 6' x 30' QUADRAPOLE | STOP BAR PRESENCE DETECTION (SIGNALIZED AND UNSIGNALIZED APPLICATIONS) | LOW CROSS TALK GOOD PRESENCE DETECTION | HIGH INSTALLATION COST RELATIVELY HIGH MAINTENANCE |
| MULTIPLE 6' x 30' QUADRAPOLE | LONG PRESENCE DETECTION ZONES | CAN IMPROVE EFFICIENCY OF ACTUATED OPERATION LOOP REDUNDANCY | HIGH MAINTENANCE TWO DETECTION CHANNELS REQUIRED VERY HIGH INSTALLATION COST |
| SINGLE OR MULTIPLE SHORT QUADRAPOLES | STOP BAR DETECTION (AROUND FULL DEPTH JOINTS, BRIDGE ENDS, ETC.) | SAME AS 6' x 30' QUADRAPOLE REDUCES JOINT RELATED FAILURES LOOP REDUNDANCY (MULTIPLE LOOPS) | HIGH MAINTENANCE TWO DETECTION CHANNELS REQUIRED (MULTIPLE) VERY HIGH INSTALLATION COST (MULTIPLE) |
| 6' x 6' SQUARE | DILEMMA ZONE DETECTORS CALL DETECTORS COUNT DETECTORS SPEED TRAPS CLOSED LOOP SYSTEM DETECTORS OCCUPANCY DETECTORS DETECTION FOR "RECALL PHASES" PRESENCE DETECTION WITH LIMITED SPACE | SENSITIVE LOOP GOOD TRUCK DETECTION LOWER INSTALLATION COST THAN LONG LOOPS GOOD POINT DETECTION GOOD ADVANCED DETECTION | HIGHER CROSSTALK THAN QUADRAPOLE POOR PRESENCE DETECTION (MAY REQUIRE LOCKING DETECTOR OPERATION) CRITICAL PLACEMENT |
| 6' RECTANGULAR | SAME AS 6' x 6' SQUARE IN WIDE LANES RAMP DETECTORS | SAME AS 6' x 6' SQUARE FULL COVERAGE OF LANES WIDER THAN 12' | SAME AS 6' X 6' SQUARE |
| 6' x 6' DIAMOND | SAME AS 6' x 6' SQUARE DETECTION IN HIGH TRUCK AREAS | SAME AS 6' x 6' SQUARE GOOD DETECTION OF HIGH BED TRUCKS | SAME AS 6' x 6' SQUARE HIGHER CROSSTALK THAN SQUARE DETECTOR MAY NOT WORK IN NARROW LANES |