Cathodic System Evaluation

| Z o n e # | Section A | Section B |
| --- | --- | --- |
|  | Rectifier Settings | Ref. Cell and Probe | Depolarization Readings |
|  | Input Voltage | Input Current | Input Current Density | On Potential (millivolt) | Instant Off Potential | Rebar Probe | 4 Hr. Off Potential (millivolt) | Shift in Potential (millivolts) | Revised Current (amps) |
| 1 | 6.8 | 2.25 | 1.50 | -550 | -510 | + | -400 | -110 | 2.3 |
| 2 | 9.0 | 3.00 | 2.00 | -492 | -460 | + | -285 | -175 | 2.5 |
| 3 | 6.9 | 2.30 | 1.53 | -605 | -585 | + | -470 | -115 | 2.3 |
| 4 | 5.4 | 1.80 | 1.20 | -511 | -488 | + | -380 | -108 | 1.8 |
| 5 | 4.2 | 1.40 | 0.93 | -488 | -470 | + | -380 | -90 | 1.6 |
| 6 | 6.8 | 2.25 | 1.80 | -215 | -9 | + | -40 | -155 | 1.7 |
| 7 | 25 | 0.50 | 0.40 | -390 | -370 | - | -340 | -30 | 1.7 |
| 8 | 6 | 2.00 | 1.60 | -355 | -330 | + | -210 | -120 | 2.0 |
| 9 | 5.1 | 1.70 | 1.36 | -400 | -385 | + | -290 | -95 | 1.8 |
| 10 | 7.2 | 2.40 | 1.92 | -388 | -375 | + | -200 | -175 | 1.4 |

Date:   8-1-06

Name:   John Rust

Bridge Number: 	A1527	Dir: E&W

Route:                      County:

Route	I-222	County	Royals

Location:  Over Blue River

Rectifier Serial:  XJ5-4172

Rectifier Brand Name:   PowerPlus

Air Temperature:	83

Date Let:

Deck Condition:  W                  5/27/1987

Type Anode:    Platinum

Cathodic System

(Mark Yes or No)

Broken Lead:

Zone Loc:

Exposed Lead:

Comment:

Corroded Lead:                               Yes

Meters Not  Functioning:	          Yes

Fuses Blown:

Corroded Circuit Board:                  Yes

Lightening Arrestors Blown

Power Off

Lost ID Tags

Are all zones on constant                No	--------->	If not, list zones on constant voltage                  7

Meter Type

Comments:

External Meter:     Yes

Built In Meter:

| Z o n e # | Section C |
| --- | --- |
|  | Original Settings | Fixed Design Parameters |
|  | Original On Potential | Original Input Current | Zone Size (Sq. Ft.) | Input Current Density (ma/sf) | Current Parameters | Potential Parameters |
|  |  |  |  |  | Lower | Upper | Lower | Upper |
| 1 | _-490 | 2.25 | 1500 | 1.50 | 0.75 | 3.00 | -294 | -686 |
| 2 | -472 | 3.00 | 1500 | 2.00 | 0.75 | 3.00 | -283 | -661 |
| 3 | -550 | 2.30 | 1500 | 1.53 | 0.75 | 3.00 | -330 | -770 |
| 4 | -458 | 1.80 | 1500 | 1.20 | 0.75 | 3.00 | -275 | -643 |
| 5 | -498 | 1.40 | 1500 | 0.93 | 0.75 | 3.00 | -299 | -697 |
| 6 | -307 | 2.25 | 1250 | 1.80 | 0.63 | 2.50 | -184 | -430 |
| 7 | -460 | 0.50 | 1250 | 0.40 | 0.63 | 2.50 | -276 | -644 |
| 8 | -355 | 2.00 | 1250 | 1.60 | 0.63 | 2.50 | -193 | -451 |
| 9 | -510 | 1.70 | 1250 | 1.36 | 0.63 | 2.50 | -306 | -714 |
| 10 | -412 | 2.40 | 1250 | 1.92 | 0.63 | 2.50 | -247 | -575 |

# Text boxes

Make comments on overall appearance of the system or any other problems.

Rectifier cabinet rusty.  Mowers have broken conduit at cabinet.

Zone 7 appears to have major problems.

Engineer’s comments from main database on Section C, changes in original set up of system, or changes made in operating parameters when new input currents set.